# ROM32X1

32-Deep By 1-Wide ROM

ROM32X1  is a 32-word by 1-bit read-only memory.  The data output (O) reflects the word selected by the 5-bit address (A4-A0).  The ROM is initialized to a known value during configuration with the INIT=value parameter .The value consists of eight hexadecimal digits that are written into the ROM from the most-significant digit A=1FH to the least-significant digit A=00H. For example, the INIT=10A78f39 parameter produces the data stream

0001  0000  1010  0111  1000  1111  0011  1001

An error occurs if the INIT=value is not specified. Refer to the appropriate CAE tool interface user guide for details.